## Slide 1
μ-MuZero: Model-Based RL for Autonomous Micro-Robotic Surgery
A Safety-Constrained, Stochastic Variant of MuZero for Optical Micromanipulation
Hamlyn Centre for Robotic Surgery | Imperial College London | 2026

## Slide 2
01
Motivation & Background

## Slide 3
Why We Need μ-MuZero
• Optical microrobots can perform cell-level surgery, but are still manually operated
• Human reaction time (~250 ms) is too slow for micro-scale fluid dynamics
• Standard RL algorithms fail at micro-scale due to three unique challenges:
• 1. Brownian motion makes dynamics inherently stochastic
• 2. Laser power has hard safety bounds — cannot explore by trial-and-error
• 3. Action space is combinatorial: 6 traps × 7 primitives = 117,649 actions
• MuZero works for board games, but not for micro-robots without adaptation

## Slide 4
The Core Insight: What Changes at Micro-Scale?
• At macro-scale: inertia dominates, dynamics are deterministic, safety is soft
• At micro-scale (low Reynolds number): viscosity dominates, Brownian motion is irreducible
• Optical force fields are highly non-linear — no closed-form model exists
• Key realization: agent must reason about UNCERTAINTY, not just expectation
• μ-MuZero learns a stochastic latent dynamics model + plans with safety-constrained MCTS

## Slide 5
02
Core Algorithm

## Slide 6
μ-MuZero Architecture
Neural Networks
• Representation h_θ: belief → latent state (256-dim)
• Dynamics g_θ: (state, action) → next state distribution
• Outputs μ and σ for Gaussian stochastic transitions
• Prediction f_θ: state → policy logits + value estimate
• All trained end-to-end via self-play in digital twin
Safety-Constrained MCTS
• Standard UCB augmented with uncertainty penalty
• Hard pruning: any action violating P > P_max is removed
• Soft penalty: phototoxicity budget tracked per episode
• Stochastic rollouts: sample K=8 trajectories from model
• Value averaged across samples for risk-sensitive planning

## Slide 7
Innovation 1: Stochastic Latent Dynamics
• Standard MuZero: deterministic transitions s' = g(s, a)
• μ-MuZero: stochastic transitions s' ~ N(μ_g, σ_g)
• Brownian displacement in 50 ms ≈ 100 nm — comparable to trap motion
• During planning, sample K trajectories and average values
• Result: policy robust to irreducible noise

## Slide 8
Innovation 2: Safety-Constrained Tree Search
• In surgery, 'explore then recover' is unacceptable
• Level 1 (Hard): MCTS prunes nodes where P > P_max
• Level 2 (Soft): cumulative phototoxicity budget penalised
• Level 3 (Epistemic): high uncertainty reduces exploration
• Constraint violation: 0.3% (μ-MuZero) vs 18% (unconstrained)

## Slide 9
Innovation 3: Factored Action Representation
• Naive space: 7^6 = 117,649 joint actions — intractable
• μ-MuZero factorises: select WHICH trap, then HOW to move
• Branching factor: 7^K → K + 6 (e.g., 117,649 → 12)
• Biologically plausible: humans attend to one trap at a time
• Enables real-time planning at 20 Hz on standard GPU

## Slide 10
Curriculum Learning for Multi-Robot Coordination
• Stage 1 (0–50K): Single-robot transport in empty workspace
• Stage 2 (50K–250K): Add static obstacles
• Stage 3 (250K–1M): Two-robot cooperative pushing
• Stage 4 (1M–2M): Three-robot micro-assembly
• Without curriculum: fails to converge after 5M steps

## Slide 11
03
System Architecture

## Slide 12
Physics-Informed Digital Twin
• Learned optical force model (NN trained on FDTD/T-matrix)
• Hydrodynamic interactions via RPY tensor
• Brownian dynamics integrated with Euler-Maruyama
• Differentiable imaging simulator for sim-to-real transfer

## Slide 13
Application Scenarios in Micro-Surgery
Single-Robot Tasks
• Cell transport: move target to micro-channel entrance
• Obstacle avoidance: navigate through cluttered tissue
• Cell sorting: separate target cells from debris
• Success rate: 91.3% (vs 67.2% scripted, 54.8% PPO)
Multi-Robot Tasks
• Cooperative transport: 3 robots push untrappable cell
• Micro-assembly: position component into slot
• Coordinated injection: multi-point drug delivery
• Success rate: 78.4% (scripted baseline: 0%)

## Slide 14
04
Experimental Validation

## Slide 15
Performance Summary vs Baselines
• Task 1 (Transport): μ-MuZero 91.3% | Scripted 67.2% | PPO 54.8% | Oracle 94.1%
• Task 2 (Obstacle): μ-MuZero 89.0% | Scripted 58.0% | Manual 62.0%
• Task 3 (Cooperative): μ-MuZero 78.4% | Scripted 0% | Manual 34.0%
• Task 4 (Assembly): μ-MuZero 68.0% | Scripted 0% | Manual 8.0%
• Phototoxicity budget: μ-MuZero 45% | Manual 68% | Scripted 82%
• Emergent behaviour: discovers 'sling-shot' manoeuvre

## Slide 16
Performance Summary vs Baselines (2)

## Slide 17
Sim-to-Real Transfer Pathway
• Step 1: Domain randomisation — randomise viscosity, temperature, noise
• Step 2: System identification — calibrate on 100 real trajectories
• Step 3: Online adaptation — MPC compensates residual model error
• Expected transfer loss: < 15% success rate drop
• Physical validation: next critical milestone at Hamlyn Centre

## Slide 18
05
Future & Impact

## Slide 19
Future Directions & Open Problems
• Real-world validation on physical optical tweezer hardware
• Meta-learning for rapid adaptation to new microrobot geometries
• Hierarchical planning: strategic (seconds) + tactical (ms) levels
• Interpretability: explain WHY the agent chose a movement
• Integration with fibre-optic endoscopes for in vivo deployment
• Regulatory pathway: certifying learned policies for human surgery

## Slide 20
References & Resources
• Schrittwieser et al. (2020). Mastering Atari, Go, chess and shogi by planning with a learned model. Nature.
• Ren et al. (2022). Machine learning-based real-time localization and automatic trapping of multiple microrobots. MARSS.
• Zhang et al. (2020). Distributed force control for microrobot manipulation via planar multi-spot optical tweezer. AOM.
• Grammatikopoulou et al. (2017). Depth estimation of optically transparent laser-driven microrobots. IROS.
• Code: github.com/yunxiao-ren/mu-muzero (upon publication)
• Contact: yunxiao.ren@imperial.ac.uk